Tokenisation

The following tokens are stored in low/high order. Each is 16 bits wide except for that representing an ASCII string.

End Token : 0000 0000 0000 0000 $0000

This token is used to mark the end of a sequence of tokens (e.g. a line of tokenised code)

ASCII String : 0000 0000 LLLL LLLL $0001-$00FF

This represents a single ASCII string. The token identifies it as a string and gives the overall length in bytes of the string.

This is not the same as the length of the string. It also includes the header word (2 bytes/1 word) and a trailing zero byte. The latter is mandatory. Hence there cannot be a string token where the length is zero.

The string is stored in such a way that the address of the following token is itself the address of the token added to the value of the token. All tokens are 16 bit, so if the length of the string, and the trailing zero byte is odd, an extra zero byte spacer must be added.

Constant Shift : 0001 CCCC CCCC CCCC $1000-$1FFF

This allows the extension of constants from 15 bits to 27 bits, e.g. enough to encompass the address range of a 65816 CPU.

When there is a constant shift, it is shifted left 15 times and added to the 15 bit “standard” constant. Processing the standard constant resets the constant shift to zero, e.g. it does not persist to the next constant.

Keywords : 001T TTTK KKKK KKKK $2000-$3FFF

These represent tokenised keywords. The numbers are not continuous though the K KKKK KKKK value is – this is the actual keyword token. TTTT identifies it’s type as follows.

0000-0111	Binary operators
0000	and	or	xor
0001	>	=	<	>=	<=	<>
0010	+	-
0011	*	/	%
0100 on	not used.

1000	Unary function
1001	Syntactic only keywords ( , ; : TO etc)
1010-1100	not used
1101	Keyword that decrements the structure level (until, wend, …)
1110	Keyword that increments the structure level (repeat, while, …)
1111	Keyword that does not affect the structure level.

Constant : ??CC CCCC CCCC CCCC $4000-$BFFF

This is two 16k groups that make 32k constants. There is 01xx xxxx xxxx xxxx and 10xx xxxx xxxx xxxx. These represent the constants 0-32767 in the lower 15 bits (e.g. the order is mixed up). The token is converted to the constant by simply dumping the 16th bit. This can be extended from 0-2^15 to 0-2^27 using the constant shift. After a constant has been extracted the constant shift is cleared.

Identifier : 11ET ACCC CCCC CCCC $C000-$FFFF

The identifier token has 2 ASCII values packed into a 16 bit word.

E is a continuation bit, if zero it marks the last token in the identifier, if 1 the token continues after this token.

TA are type bits. T is 1 if the type is a string, A is 1 if the type is an array. The post identifier characters $ and ( are included as part of the tokenisation. (So a2$( only occupies one token space)

CCC CCCC CCCC is 2 numbers from 0-44 multiplied together as 2nd Character * 45 + 1st Character. The values are :

0	filler if there is an odd number of characters / space
1-26	A-Z
27-36	0-9
37-44	Unused

Memory Blocks

Memory is divided into blocks. Blocks can be up to 64k in size. Each block must all be in the same 64k address space. They do not have to start at the start of a block, so all these address are offsets from the base address.

Offset	Contents
$0000	4 byte type ID. A Basic program has the ASCII characters for “BASC” here.
$0004	12 byte (maximum) identifying label, as prefixed string, used to identify a block by name.
$0010	Low Memory pointer. This is a 16 bit address (not offset) which is the next free byte available in low memory.
$0012	High Memory pointer. This is a 16 bit address(not offset) which is the byte after the topmost free byte.
$0020	26 Fast Variables A-Z, 4 bytes each ; so @ is at $0020 and Z is at $0074
$0080	4 x 16 word addresses which are linked lists of variables, these are in line with the TA bits, so are integer, integer array, string, string array.

$0100	The program
…	$0000 indicating end of the program
…	By convention $EEEE $EEEE is stored in the 4 bytes following the end of the program, to place a clear marker between the BASIC code and the variables.
…	First variable.
…	More variables/
…	Free unused Space. The current value of the low memory pointer is the first byte of this space.
…	Data Space. This is used for strings. Some space above this may be reserved so the program creating blocks can create identifiers.
…	End of Block. The byte after the last in the block. The High Memory Pointer is initially set to this value normally, though in testing test data may be stored above here both arrays and strings as well as tokenised names.

Program Storage

Programs are a collection of records in line number order.

The header is 2 words:

Firstly an offset to the next line. If this is zero this indicates the program end.

Secondly the tokenised line number, from 0-32767, this is stored with bit 15 cleared, e.g. in unencoded format.

The tokens making up the program line follow this, ending in the $0000 token.

Variable Storage

Variable storage immediately follows the end of program storage.

Each record occupies 6 information bytes and 2 or 4 bytes for each item of data.( 2 for strings, 4 for integers )

+0..1	The address of the next variable in the list
+2..3	The address of the identifier as a sequence of tokens (stored in program code normally).
+4..5	Highest array index for an array, 0 if non-array.
+6..	First data element.

All addresses are absolute addresses not offsets. Variables are all erased when a program is RUN or the code is edited.

Variables are stored in linked lists, ending with a next variable address (the link) of $0000. There are up to 16 hash entries for variables, and four sets of linked lists for each of the four available types.